## Slide 1
Amiga Robot — System Architecture Overview
gRPC Service Topology · Port Allocation · Control Flow · Sensor Pipeline
5
gRPC Services
6
Camera Streams
6001–50010
Port Range
3
Control States
< 50ms
Cmd Latency
10 Hz
Odom Rate
Pendant
Canbus :6001
Filter :20001
Track Follower :20101
OAK Cameras :50010
GPS :50010
Data flows left → right: Pendant triggers Canbus, which feeds Filter (odometry), Track Follower (path exec), while OAK + GPS provide perception.
Amiga Robotics | March 2026

## Slide 2
Service Port Allocation & gRPC Endpoints
Each service exposes gRPC endpoints on dedicated ports for isolation and reliability
Chart: 
| Canbus | Filter | OAK Cameras | GPS | Track Follower | Sys Monitor
Endpoints | 2 | 2 | 6 | 1 | 2 | 3
Port | 6001 | 20001 | 50010 | 50010 | 20101 | 20201
Service | Port | Protocol | Key Paths
Canbus | 6001 | gRPC | /twist, /state
Filter/Odom | 20001 | gRPC | /state
OAK Cameras | 50010 | gRPC | /left, /rgb, /right, /disparity
GPS | 50010 | gRPC | /pvt
Track Follower | 20101 | gRPC | /track, /status
System Monitor | 20201 | gRPC | /health, /metrics, /logs

## Slide 3
Control State Machine & Transition Flow
Amiga uses a state-based control model — pendant sets AUTO_READY, software activates AUTO_ACTIVE
MANUAL (State 1)
E-STOP (State 2)
CRUISE (State 3)
AUTO_READY (State 4)
AUTO_ACTIVE (State 5)
Pendant Switch
Pendant Switch
/twist cmd
E-Stop / Timeout
Chart: 
| MANUAL | AUTO_READY | AUTO_ACTIVE | CRUISE | E-STOP
Time % | 10 | 15 | 60 | 10 | 5
Typical operational time distribution

## Slide 4
Sensor Pipeline — OAK Camera & GPS Throughput
6 camera streams + GPS feed processed at varying frame rates and bandwidths
Chart: 
| Left Mono | RGB Center | Right Mono | Disparity | IMU | GPS PVT
Frame Rate (Hz) | 30 | 30 | 30 | 15 | 100 | 10
Bandwidth (MB/s) | 12 | 36 | 12 | 8 | 0.5 | 0.1
Chart: 
| RGB Center | Left Mono | Right Mono | Disparity | IMU | GPS
Bandwidth | 36 | 12 | 12 | 8 | 0.5 | 0.1
Bandwidth Distribution
RGB stream uses 52% of total sensor bandwidth → Compression priority #1

## Slide 5
ROS2 Bridge — Message Flow & Latency Analysis
gRPC-to-ROS2 bridge converts Amiga messages with minimal overhead
Chart: 
| Twist Cmd | Canbus State | Odom/Filter | Camera Frame | GPS PVT
gRPC Call (ms) | 5 | 3 | 4 | 8 | 6
Serialization (ms) | 2 | 4 | 3 | 12 | 2
ROS2 Publish (ms) | 1 | 2 | 2 | 5 | 1
Network (ms) | 3 | 3 | 3 | 15 | 4
Amiga Service
gRPC Client
Bridge Node
ROS2 Topic
Subscriber Node
~5ms
~3ms
~2ms
~1ms
Total end-to-end: 11–40ms depending on message type. Camera frames are the bottleneck.

## Slide 6
System Health & Operational Metrics
Real-time monitoring via System Monitor service on port 20201
Chart: 
| T+0s | T+10s | T+20s | T+30s | T+40s | T+50s | T+60s | T+70s | T+80s | T+90s
CPU % | 35 | 42 | 55 | 48 | 62 | 58 | 45 | 50 | 53 | 47
Memory % | 60 | 61 | 62 | 63 | 65 | 64 | 63 | 64 | 65 | 64
Net (MB/s) | 40 | 45 | 68 | 55 | 72 | 65 | 50 | 58 | 60 | 52
Canbus
HEALTHY
Filter
HEALTHY
OAK Cameras
WARN
GPS
HEALTHY
Track Follower
IDLE
ROS2 Bridge
HEALTHY
OAK WARN: Frame drops detected on disparity stream (>5% loss)
Amiga Robotics | March 2026